## Slide 1
Smart DJ Booth
Real-time DJ feedback powered by ESP32 crowd sensing and sound intelligence
• A demo-first booth intelligence system for live event environments
• Built to work in real hardware mode and fallback demo mode
Smart DJ Booth | Demo-Ready ESP32 Intelligence

## Slide 2
The Problem
DJs usually react to the room by instinct alone
• No simple live system tells the DJ whether the crowd is building, hyped, fading, or too loud
• That creates missed moments, delayed adjustments, and weaker audience engagement
• Smart DJ Booth turns crowd conditions into clear real-time booth feedback
Smart DJ Booth | Demo-Ready ESP32 Intelligence

## Slide 3
The Solution
A compact ESP32-based sensing engine for booth intelligence
• VL53L0X estimates crowd density from distance to the booth
• INMP441 captures room energy from sound intensity
• ESP32 processes both signals into simple states: LOW, GOOD, HYPE, TOO LOUD
• Output is designed for serial monitoring today and dashboard integration later
Smart DJ Booth | Demo-Ready ESP32 Intelligence

## Slide 4
System Architecture
Simple hardware, clear logic, strong demo story
• Sensors -> ESP32 -> smoothing + decision engine -> serial output
• Density is derived from measured distance
• Energy is derived from processed microphone amplitude
• The same output contract supports both real hardware and simulation mode
Smart DJ Booth | Demo-Ready ESP32 Intelligence

## Slide 5
Why Demo Mode Matters
The project stays presentation-ready even when hardware is unstable
• Fallback mode keeps the full product story alive during hardware issues
• Five built-in scenarios simulate realistic booth conditions
• Warmup Room, Crowd Surge, Peak Hour, Too Loud Alert, Late Night Dip
• This protects demos, testing, and future dashboard development
Smart DJ Booth | Demo-Ready ESP32 Intelligence

## Slide 6
Current Build Status
A working backend path exists today
• Integrated ESP32 firmware is ready in Arduino IDE and VS Code workflows
• Automatic and forced demo fallback are built into the main sketch
• Sensor test sketches are prepared for VL53L0X and INMP441 bring-up
• Structured output is ready for a dashboard phase when needed
Smart DJ Booth | Demo-Ready ESP32 Intelligence

## Slide 7
Next Steps
From stable demo to full live deployment
• Fix board connectivity and validate both sensors independently
• Switch the integrated sketch from demo mode to live mode
• Tune thresholds in a real room environment
• Add a polished dashboard layer for client-facing visuals
Smart DJ Booth | Demo-Ready ESP32 Intelligence